Wall-mount AC-DC power supplies with enhanced home healthcare design

May 26, 2022 – XP Power has released three new series of IP22-rated wall-mount power supplies that deliver significant benefits to the rapidly growing home healthcare market. The devices suit a wide range of cost-sensitive industrial and medical applications while maintaining industry-leading performance.

Increasingly, patient monitoring is being conducted in the home or workplace for convenience or to reduce pressure on hospitals. These new power solutions are specifically designed to operate down to 80VAC to allow for transmission line loss in remote non-hospital locations, whilst maintaining a reliable DC output.

The AMF family of wall plug adaptors offers power levels of 18W (AMF18), 24W (AMF24), and 36W (AMF36) with a single output covering all common voltages between 5.0V and 48.0V, allowing designers to select the ideal device for a wide variety of applications.

All AMF devices are fully approved to a variety of medical, home healthcare, and IT standards, including EN55011, IEC60601, and UL 62368. As the power supply is external, the design of any equipment is dramatically simplified, and the time, cost, and risk associated with gaining approvals are eliminated.

As Class II devices, they can operate safely in environments where the integrity of the safety of earth is not known. The devices are sealed to IP22, allowing the power supply to be cleaned and / or disinfected with reduced risk of electric shock. The AMF power supplies offer 2 x MOPP (Means of Patient Protection), thereby ensuring end-user safety in the unlikely event of a power-related issue. Moreover, leakage current is less than 50(A, allowing safe operation in applications where applied parts may be connected to the patient.

All AMF power supplies operate over an extended input voltage range of 80 to 264VAC, allowing worldwide operation with an additional margin for regions where the voltage may fluctuate. A range of interchangeable AC connectors ship with every device, thus allowing the power supply (and any associated medical equipment) to be used globally.

The AMF18, AMF24, and AMF36 series are available from Digi-Key, Distrelec, Farnell, Mouser, RS Components, TME Electronic Components, approved regional distributors, or direct from XP Power and offer a 3-year warranty.

+++Ends

For press enquiries:

Maria Alonso, Publitek

Tel: +44 1582390980

Email: maria.alonso@publitek.com

For reader enquiries:

UK:

Paul Garner

Tel: +44 1189 845 515

Email: pgarner@xppower.com

Austria, Germany & Switzerland:

Nico Kagel

Tel: +49 421 639 330

Email: nkagel@xppower.com

Denmark & Finland:

Ture Johansen

Tel: +45 4342 3833

Email: tjohansen@xppower.com

France:

Marc Crosnier

Tel: +33 678 753 790

Email: mcrosnier@xppower.com

Italy:

Mauro Roncarati

Tel: +39 0270 103 517

Email: mroncarati@xppower.com

Norway:

Tore Spildrejorde

Tel: +47 6394 6018

Email: tspildrejorde@xppower.com

Spain & Portugal:

Julio Canalís

Tel: +34 932 633 354

Email: jcanalis@vencoel.com

Sweden:

Mikael Nilsson

Tel: +46 855 536 700

Email: mikael.nilsson@xppower.com

About XP Power:

XP Power is committed to being a leading provider of power solutions, including AC-DC power supplies, DC-DC converters, High Voltage power supplies and RF power supplies. With ISO9001:2008, XP Power offers total quality, from in-house design through to manufacturing facilities around the world. The company offers the widest range of power products available from one source and unrivalled technical and customer support, aiding both vendor consolidation and cost reduction programmes. XP Power has 24 sales offices throughout Europe, North America, and Asia.

XP Power Ltd (LSE:XPP), a London Stock Exchange FTSE 250 listed public company, has design centres in North America (Massachusetts, New Jersey & California) and Singapore, which also serves as the company’s headquarters. Manufacturing facilities are located in North America, Vietnam, and China. The design teams push back the boundaries of cost and technology, providing market leading power solution products. Local application teams provide expert technical support to help customers integrate and use XP Power products worldwide. Find more information about how XP Power are powering innovation at www.xppower.com