## Slide 1: Extending InnoSwitch™3 IC Families With GaN Switches
July 25, 2019

## Slide 2: InnoSwitch3 (CE/CP/Pro) ICs Achieve > 100 W
InnoSwitch3 silicon transistors are highly effective up to 65 W
  Size 7 is the lowest RDS(ON) silicon MOSFET that will fit in the InSOP-24 package
PI GaN switches provide more power
  Lower RDS(ON) per unit area
  Lower switching losses
InnoSwitch3-CP – constant power
InnoSwitch3-EP – for open frame
InnoSwitch3-Pro – digital control
GaN switches

## Slide 3: Applications with Size AND Efficiency Needs
Aftermarket USB PD adapters
High-end cellphone chargers and other mobile devices
Notebook adapters
Products with size OR efficiency needs
  Appliances, TVs, server standby, AIO PCs, video games
Applications requiring feature benefits of InnoSwitch, but need more power

## Slide 4: Making GaN Easy to Use
GaN transistors are better than silicon
  More efficient, cooler, smaller power supplies
  Leading the way to “no-heatsink” designs at high power levels
GaN transistor technology is the future for power conversion
Our strategy is to enclose and protect the GaN device within our ICs
  Engineers see significant performance benefits
  But won’t otherwise notice a change

## Slide 5: Consistent, Familiar and Easy to Implement
Simple flyback circuit topology
Use identical SMPS design flows for silicon and GaN InnoSwitch3 ICs
Identical switching frequency
External components scale for power
Switching waveforms are very similar
No unusual behaviors or concerns
  EMI Standard techniques
  ESD No different from silicon

## Slide 6: GaN Increases InnoSwitch3 Efficiency and Power
RDS(ON) (Ω) – Typical (25 °C)
Output Power (W)

## Slide 7: Wide Power Range and High VDS(MAX)
Product | Adapter Rating (W) | InnoSwitch3 |  |  |  | InnoSwitch3-Pro |  | 
 | 85-265 VAC | 650 V | 725 V | 750 V | 900 V | 650 V | 725 V | 750 V
INN36y2C | 10 |  |  |  |  |  |  | 
INN36y3C | 12 |  |  |  |  |  |  | 
INN36y4C | 15 |  |  |  |  |  |  | 
INN3xy5C | 22 |  |  |  |  |  |  | 
INN3xy6C | 27 |  |  |  |  |  |  | 
INN3xy7C | 40 |  |  |  |  |  |  | 
INN3xy8C | 50 |  |  |  |  |  |  | 
INN3xy9C | 65 |  |  |  |  |  |  | 
INN3xy0C | 75 |  |  |  |  |  |  | 
X = InnoSwitch3 Product family
2 = CP
3 = Pro
6 = EP
Y = Primary Switch Voltage Rating
6 = 650 V
7 = 725 V / 750 V
9 = 900 V

## Slide 8: GaN Switches Significantly Reduce Losses
MOSFET output capacitance is discharged through itself at turn-on
  Parasitic capacitances are proportional to the size of the MOSFET
  Bigger MOSFET = more switching loss
    Also lower RDS(ON) means less conduction loss
f . COSS .V2
2
P(Loss) =
f = Switching frequency
V = Peak of VAC ~ 400 V
Gate
Drain
Source
COSS = CDS + CGD
CDS

## Slide 9: Switching Losses Increase with FET Size Conduction Losses Decrease with FET Size
Conduction losses and switching losses work in opposite directions
Power lost with conventional MOSFET
Switching Loss
(MOSFET)
Total Power Loss (MOSFET)
(I2R)
(CV2)

## Slide 10: GaN Switches Change the Curve
Conduction losses and switching losses work in opposite directions
Power lost with GaN Technology
Switching Loss
GaN
Power lost with conventional MOSFET
Total Power Loss GaN
Total Power Loss (MOSFET)

## Slide 11: GaN-Based Design Achieves 95% Full-Load Efficiency -Allows Elimination of Heatsinks from Adapter Designs
DER-747 (65 W, 20 V Adapter): Full-load efficiency is 95% at 230 VAC and 94% at 115 VAC

## Slide 12: GaN High Efficiency Also Improves Performance Across Load for 60 W USB PD
Same high-efficiency-across-load as standard InnoSwitch3
  Ideal for high-power USB PD applications
Average efficiency is 92.49% at 115 VAC and 93.24% at 230 VAC

## Slide 13: Available GaN Reference Designs
InnoSwitch3 for USB PD baseline design
  DER-601 60 W USB PD (WT6635P)
  DER-602 100 W USB PD (WT6635P)
  DER-747 65 W Non-USB PD adapter
InnoSwitch3-Pro for USB PD + PPS design
  DER-802 60 W USB PD (WT6635P)
  DER-803 60 W USB PD (VP302)
  DER-805 100 W USB PD (VP302)

## Slide 14: Summary: GaN – Powerful, Efficient, Reliable
PI GaN devices deliver more power
  Reduced on-resistance
  Lower switching loss
Circuit operation indistinguishable from one using silicon devices
Manufacturing processes developed and maintained by PI
  Working with established partners
Industry-leading GaN qualification process
65 W Reference Design Using INN32X9C

## Slide 16: Q&A Slides

## Slide 17: Supply Chain Questions
The technology we are using is proprietary to Power Integrations
PI GaN transistor fabrication done at existing silicon fab partners
InnoSwitch3 Size 9 and 10 devices use the same assembly and test facilities as silicon InnoSwitch3 parts
Comprehensive technology qualification meets exacting PI standards

## Slide 18: GaN Qualification Mirrors Silicon Product Qual. Protocol
 | Test Description | Symbol | Test Method | InnoSwitch3 | InnoSwitch3 (GaN)
Fab Process | Preconditioning & Moisture Sensitivity Level | PC | JESD22-A113 | MSL3 | MSL3
 |  |  | JEDEC J-STD-020 | MSL3 | MSL3
 | Temperature Humidity Bias | THB | JESD22-A101 | Multiple units, multiple lots | Multiple units, multiple lots
 | Temperature Cycling | TC | JESD22-A104 | Multiple units, multiple lots | Multiple units, multiple lots
 | High Temp. Storage Life | HTSL | JESD22-A103 | Multiple units, multiple lots | Multiple units, multiple lots
 | Dynamic Operating Life | DOPL | JESD22-A108 | Multiple units, multiple lots | Multiple units, multiple lots
Fab and Package | Highly Accelerated Life Test | HALT | JESD22-A104 | Multiple units, multiple lots | Multiple units, multiple lots
 | High Temp. Reverse Bias | HTRB | JESD22-A108 | Multiple units, multiple lots | Multiple units, multiple lots
Packaging Process | Preconditioning | PC | JESD22-A113 | Multiple units, multiple lots | Multiple units, multiple lots
 | Moisture Sensitivity Level | PC | JEDEC J-STD-020 | Multiple units, multiple lots | Multiple units, multiple lots
 | Temperature Humidity Bias | THB | JESD22-A101 | Multiple units, multiple lots | Multiple units, multiple lots
 | Temperature Cycling | TC | JESD22-A104 | Multiple units, multiple lots | Multiple units, multiple lots
 | High Temp. Storage Life | HTSL | JESD22-A103 | Multiple units, multiple lots | Multiple units, multiple lots

## Slide 19: PI’s GaN is Extremely Robust
380 VDC
~530 VDC
650 V = VMAX(continuous)
750 V = VMAX(non-repetitive)
Typical margin (150 V)
Gives de-rating of > 80%
Primary Switch Voltage Stress (264 VAC)
Safe Surge Voltage Region (SSVR)

## Slide 20: Customers
We do not release the names of our customers
The following customers have been identified by Yole in their report
  Anker, Aukey, Ravpower
We are not releasing shipping volumes, backlog or GaN-based revenue information at this time